Accident Cause Analysis Checklist

Note:	This checklist is a guide for investigating the cause of an accident or near accident.

| Immediate Cause | Possible Underlying Causes | Management Responsibilities |
| --- | --- | --- |
| Poor housekeeping | Inadequate housekeeping standard Inadequate storage Excess accumulation | Set high housekeeping standard Provide storage Dispose of excess |
| Improper use of tools, equipment, facilities | Lack of skill, knowledge Lack of proper procedures Shortcutting Improvising | Train employees Establish procedures Enforcement of proper procedures Provide sufficient tools, etc. |
| Unsafe or defective tools, equipment, facilities | Not recognized as unsafe Poor design or selection Poor maintenance | Train employees Design, selection planning, and review Establish preventive maintenance |
| Lack of proper procedures | Omissions Errors by designer Errors by supervisor | Provide procedures Conduct safety analysis Instruct supervisors |
| Improvising unsafe procedures | Lack of proper procedure Failed to follow prescribed procedure | Establish safe procedures Enforce proper procedures |
| Failure to follow prescribed procedures | Need not emphasized Procedures unclear | Enforce proper procedures Provide good procedures |
| Job not understood | Instructions complex Error by supervisor | Simplify instructions Re-train employee Train supervisors |
| Lack of proper tools, equipment, facilities | Need not recognized Inadequate supply | Conduct safety analysis Provide equipment, materials, tools Supervise employee |
| Lack of guards, safety devices | Need not recognized Not provided Deliberate removal | Conduct safety analysis Provide required safety equipment Discipline |
| Lack of protective equipment, clothing | Needs not recognized Did not know how or when to use Inadequate availability Deliberate failure to use | Conduct safety analysis Train employees Provide safety equipment Discipline |
| Exceeding prescribed limits, load speed strength, etc. | Warnings inadequate Instructions inadequate Lack of comprehension Deliberate | Emphasize warnings Re-train employee Ask for feedback Discipline |
| Inattention; neglect of obvious safe practice | Lack of motivation Employee rushed Insufficient work (employee bored) Inadequate comprehension | Enforce safety rules or procedures Reevaluate job process Reevaluate work assignments Review employee and placement |
| Fatigue, reduced alertness, hypnosis | Excessive job demands Personal problems or lifestyle affect job performance | Reevaluate job process and staffing Review employee selection and placement Refer to Human Resources and EAP |
| Misconduct; deliberate failure to use protective clothing | Low morale Poor attitude | Counsel employee Administer progressive discipline |